## Slide 1: ACPI-based vCPU hotplug support on arm64 Kata-containers
Justin He justin.he@arm.com
2019 Oct CLK2019

## Slide 2: Background
Kata runtime
VM
1 VCPU
128M memory
VM
n VCPUs
2048 M memory
Mem/CPU hotplug
via gRPC
Update Resource
Kata agent
Notes: To speed up the vm creation, kata will start a vm with limited resources, such as 1 vcpu, 128 mb memory
The memory hotplug
Then we come to the cpu hotplug
vcpus will be dynamically assigned when kata-containers wants to update resources

## Slide 3: CPU hotplug requirement Kata-containers on arm64
cpu resource update for “docker run” cmd in Kata-containers project. e.g. $ docker run --runtime=kata-runtime -ti --cpus 2 debian bash $ docker update --cpus 4 foo
Obstacles:
  Each CPU has a notional point to point link to the interrupt controller (to the redistributor, to be precise), and this entity must pre-exist.
  When the vgic initializes its internal state it does so based on the number of VCPUs available at the time.
Notes: Here are some comments from Mark and Christoffer:
The conclusion is that : the vcpu number should be available before vgic initialized

## Slide 4: Online/offline solution
Kata qmp
qemu
Guest vm
start guest with
-smp 4 -append “maxcpus=1”
start cpus(1 online,3 offline)
query_hotpluggable_cpus
return cpu node info
device_add/del cpu
online/offline cpus by gRPC
Send DEVICE_DELETED event
Notes: 1. When the changed qemu starts a vm with -smp 4 -append “maxcpus=1”, It can create 4 cpus in
device-tree, and set 3 as pluggable. This work around the vcpu re-init obstacle at kvm side.
2. Then the guest kernel will be booted with 4 cpus, but let 3 be offline
3. use qmp cmd "query_hotpluggable_cpus" to get the pluggable cpus info in the
guest.
4. When qmp cmd "device_add" is triggered, guest will be notified to set one
pluggable cpus to be online.
5. Use gRPC req “onlineCPU/offlineCPU” to set the wanted cpus to be online/offline at kata agent side.

## Slide 5: Disadvantages:
  the docker container density on arm64.
  an orchestration workaround that neither the hypervisor nor the architecture support.
  security drawback for the containers

## Slide 6: ACPI-based vCPU hotplug support on arm64
Protocol depends on platform
  ACPI (x86 & ARM)
  PAPR events (POWER)
Some assumptions
  fdt vcpu hotplug will not be covered
  hotplug add firstly, then hotplug remove
  TCG mode firstly, then kvm mode (vgic initialization limitation)

## Slide 7: Steps to support ACPI-based solution
Kernel (guest kernel)
  Change scanning process for ACPI tables (MADT...) for pluggable Cpus,
  Reserve the gic resource for maximum possible cpu number
  Kernel receives the ACPI event interrupt, then registers a new cpu, start the new cpu by PSCI cpu_on call and add it into scheduler system
  Relax the limitation in vgic initialization of Arm64 kvm

## Slide 8: Steps to support ACPI-based solution
Qemu changes
  Implement GED device
  Add vcpu hotplug infrastructure virt_new_cpu, virt_cpu_plug, preplug
  Map the mp_affinity to cpu id.
  Build ACPI tables, set the flag in MADT
  Send ACPI GED event to notify the new vcpu
  Reserve the MaxCpus vcpu for gic initialization
  Vcpu thread will be dynamically allocated/removed

## Slide 9: Status and future plan
Status
  Kernel (guest kernel)
    Huawei (Wang xiongfeng) proposed a RFC series in 2019 June
  Qemu changes
    codes are done in TCG/gicv2 mode.
Future plan
  Support kvm/gicv3 mode at qemu side
  Do not conflict the codes with support ACPI cpu hotplug physically on host