## Slide 1: Dm-writecache: a New Type Low Latency Writecache Based on NVDIMM
2019.10.12
Huaisheng Ye | 叶怀胜
v3

## Slide 2: Agenda
NVDIMM
Device Mapper
The structure of dm-writecache
Performance comparison with dm-cache
Customized solution – Ceph OSD bluestore
Patchset from Lenovo
Q&A

## Slide 3: NVDIMM
NVDIMM-N
NVDIMM-F
AEP (Intel 3D XPoint)
Hard Disk Drives
NVDIMM
NVMe & NAND SSD
DDR
CPU
Highest Cost
Shortest Latency
Byte Addressable
Core
L1
L1
L2
L3
Core
L1
L1
L2
Memory Controller
Memory Controller
NVDIMM
NVDIMM
ADR
(Asynchronous DRAM Refresh)
CLWB
CLFLUSH
CLFLUSHOPT

## Slide 4: Device Mapper
dm-linear
dm-multipath
dm-mirror
dm-snapshot
dm-cache v3.9
dm-writecache v4.18
……
Core device-mapper
Target interface
linear
mirror
snapshot
cache
writecache
Control interface
Block interface
ioctl
FS interface
Userspace tools (dmsetup & LVM2)

## Slide 5: How dm-writecache works
pmem or ssd
HDD
Write/Read Hit
CPU
Writeback
dm-writecache
Read Miss
No Warm-up!

## Slide 6: dm-writecache structure
superblock
entries
block_start
block_size
12
rb_node
high_watermark
low_watermark
autocommit_timer
autocommit_blocks
lru
lru
lru
lru
lru
lru
lru
freelist
struct dm_writecache
…
…
wc_entry
5
3
17
15
19
15’

## Slide 7: Cache lines
Page Tearing
Line 0
Line 1
Line 2
Line 3
Line 4
Line 5
Line 6
…
Line 63
…
Line 0
Line 1
Line 2
Line 3
Non-consistent Line
Consistent Line
DRAM
Cache Lines
Line 63
Line 56
Line 0
Line 7
Direct mapped Cache fill: (a simple example of CPU cache lines)
  modern x84_64 has 64 bytes in each cache line, one 4K Page is divided into 64 lines

## Slide 8: dm-writecache vs others
  dm-writecache specialty:
Dedicated to Persistent memory and fast SSD
dm-cache, B-cache, Flushcache: no DAX, no byte addressable capability for NVDIMM.
dm-writecache benefits:
No warm-up time for Writes
Sorting blocks partially when writeback
Compared with PMDK: totally transparent, no modification of Apps

## Slide 9: Parameters of dm-writecache
No | Parameter Name | Explanation | Default
1 | Cache type | Type of cache device – p or s | p
2 | Original device | The underlying device that will be cached | (/dev/sd*)
3 | Cache device | The cache device | (/dev/pmem*)
4 | Block size | 4096 is recommended and the maximum block size is the page size | 4096
5 | Number of optional | The number of optional parameters | 0
6 | Start sector | Offset from the start of cache device in 512-byte sectors | 0
7 | High watermark | Start writeback when the number of used blocks reach this watermark | 50
8 | Low watermark | Stop writeback when the number of used blocks drops below this watermark | 45
9 | Writeback jobs | Limit the number of blocks that are in flight during writeback. Setting this value reduces writeback throughput, but it may improve latency of read requests | Unlimited
10 | Auto commit blocks | When the application writes this amount of blocks without issuing the FLUSH request, the blocks are automatically commited | Pmem: 64 SSD: 65536
11 | Auto commit time | Autocommit time in milliseconds. The data is automatically commited if this time passes and no FLUSH request is received | 1000
12 | FUA | Applicable only to persistent memory - use the FUA flag when writing data from persistent memory back to the underlying device | On

## Slide 10: HW Platform for testing
Thinksystem SR630
CPU Intel(R) Xeon(R) Gold 6240 CPU @ 2.60GHz * 2
MEM 16G * 8
NVDIMM Intel Optane DCPMM 128G * 4
HDD 300GB 15K 12Gbps SAS 2.5" HDD (JBOD)

## Slide 11: Performance comparison with dm-cache
dm-writecache: (fsdax mode)
# lvcreate -n hdd_wc -L 4G vg /dev/sda1
# lvcreate -n cache_wc -L 1G vg /dev/pmem0
# lvchange -a n vg/cache_wc
# lvconvert --type writecache --cachevol cache_wc vg/hdd_wc
dm-cache: (sector mode)
# lvcreate -n hdd_s -L 4G vg /dev/sda1
# lvcreate -n cache_s -L 1G vg /dev/pmem0.2s
# lvconvert --type cache --cachevol cache_s vg/hdd_s --chunksize=32 --cachemode writeback
Eg.
# fio -filename=/dev/vg/hdd_wc -direct=1 -iodepth=20 -rw=randwrite -ioengine=libaio -bs=4k -loops=1
-size=2g -group_reporting -name=mytest1 --write_iops_log=fio-randwrite-wc --log_avg_msec=1000
Namespace modes:
fsdax
sector
raw
devdax

## Slide 12: 4k randwrite (Full View)
Chart: randwrite
Chart: IOPS
Cache Exhausted
But 50% has been done!
Seconds

## Slide 13: 4k randwrite
Chart: randwrite
Chart: Time consuming
dm-writecache | 65
dm-cache | 697
hdd | 533
The smaller the better
Cache Exhausted
But 50% has been done!
981
366
Needs migration
in dm-cache
Seconds
Even cache exhausted, still get enhancement by sorting blocks for writeback

## Slide 14: 4k write
Chart: seq write
dm-writecache | 169501 | 121425 | 94460 | 75652 | 58797
dm-cache | 1111 | 3468 | 12446 | 1275 | 42715 | 47097 | 1364 | 1979 | 2829 | 3823 | 2853 | 1765 | 3275 | 32819 | 56642 | 1555 | 3237 | 4227 | 1418 | 58479 | 31197 | 981 | 51355 | 39184 | 12052 | 59881
hdd-pure | 60337 | 58563 | 60443 | 60060 | 59901 | 59889 | 60043 | 59786
Chart: Time consuming
dm-writecache | 5
dm-cache | 26
hdd | 8
Seconds
The cost of warming-up
Almost the same

## Slide 15: 4k randread
Chart: Time consuming
dm-writecache | 556
dm-cache | 415
hdd | 573
Chart: randread
Seconds
Remap to original device when Read miss
dm-cache warm-up

## Slide 16: 4k read
Chart: seq read
dm-writecache | 59964 | 60255 | 60350 | 60382 | 60276 | 60504 | 60547 | 60215
dm-cache | 42739 | 48674 | 48741 | 49334 | 59082 | 60135 | 59915 | 60163 | 60040
hdd-pure | 59487 | 60174 | 60544 | 60059 | 59810 | 59981 | 59970 | 59849
Chart: Time consuming
dm-writecache | 8
dm-cache | 9
hdd | 8
Seconds
warm-up

## Slide 17: How does Lenovo play over NVDIMM long term
Hardware
Firmware
ndctl, ipmctl
PMDK (nvml)
OS (RHEL 7, 8)
Device mapper
LVM
Ceph and others
Customized and Optimized Solutions

## Slide 18: Customized Ceph OSD
PMEM
Ceph Bluestore
MetaData{db,wal}
BlueFS
RocksDB
Data
ObjectStore
Ceph OSD
Data
PMEM
HDD
Logic Device
NVDIMM serves as pmem writecache for HDD device
Performance boost for random write
No code change in Ceph
POC is ready
dm-writecache
PMEM
Sector
fsdax

## Slide 19: Prepare Logical volume for Ceph OSD
dm-writecache:
# lvcreate -n osd0.wal -L 4G vg-ceph /dev/pmem1.1s
# lvcreate -n osd0.db -L 4G vg-ceph /dev/pmem1.1s
# lvcreate -n osd0 -L 40G vg-ceph /dev/sdb1
# lvcreate -n osd0.cache-wc -L 10G vg-ceph /dev/pmem1
# lvchange -a n vg-ceph/osd0.cache-wc
# lvconvert --type writecache --cachevol osd0.cache-wc vg-ceph/osd0
# ceph-deploy osd create --data vg-ceph/osd0 --block-db vg-ceph/osd0.db --block-wal vg-ceph/osd0.wal --bluestore target01
--------------------------------------------------------------------------------------------------------------
dm-cache:
# lvcreate -n osd1.wal -L 4G vg-ceph /dev/pmem1.1s
# lvcreate -n osd1.db -L 4G vg-ceph /dev/pmem1.1s
# lvcreate -n osd1 -L 40G vg-ceph /dev/sdb1
# lvcreate -n osd1.cache-s -L 10G vg-ceph /dev/pmem1.1s
# lvconvert --type cache --cachevol osd1.cache-s vg-ceph/osd1 --chunksize=32 --cachemode writeback
# ceph-deploy osd create --data vg-ceph/osd1 --block-db vg-ceph/osd1.db --block-wal vg-ceph/osd1.wal --bluestore target01
--------------------------------------------------------------------------------------------------------------
# fio -filename=/dev/rbd0 -direct=1 -iodepth=20 -rw=randwrite -ioengine=libaio -bs=4k -loops=1 -size=20g
-group_reporting -name=mytest1 --write_iops_log=fio-randwrite-s-ceph-01 --log_avg_msec=1000

## Slide 20: 4k randwrite for Ceph rbd
Chart: ceph-randwrite
Chart: Time consuming
dm-writecache | 703
dm-cache | 5863
Seconds
Cache Exhausted

## Slide 21: Patchset from Lenovo OS team
Lenovo has contributed 26 patches to kernel community
Most of them belong to NVDIMM and Device mapper subsystem
Continues to submit features to community
Latest patchset is performance optimization, saves 50+% time on writeback_all
https://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux.git/commit/?id=5229b4896e8f32bda4bfe29ff91e594ae7aa8a75
https://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux.git/commit/?id=f8011d334426cee77276a1038b627b5cb0470258
https://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux.git/commit/?id=09f2d6563055b8ff0948cefb8911a4de0d559963
https://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux.git/commit/?id=6d1959138c8bdaf69f1116c86c77e6733db6ab34

## Slide 22: Patchset for writeback_all
struct writeback_list wbl;
lru
lru
lru
lru
lru
lru
lru
freelist
struct writecache
…
…
wc_entry
12
rb_node
5
3
17
15
19
Chart: Time consuming when writeback_all
original | 101.848
patched | 44.893
The smaller the better

## Slide 23: Reference
https://www.kernel.org/doc/html/latest/admin-guide/device-mapper/writecache.html
https://ceph.com/resources/
https://pmem.io/documents/NVDIMM_DriverWritersGuide-July-2016.pdf
https://docs.pmem.io/ndctl-users-guide
https://docs.pmem.io/ipmctl-user-guide
https://github.com/pmem/ndctl

## Slide 24: Q&A
WeChat
Any suggestion and comment is welcome!